Performance Evaluation of Digital Modulation Techniques Used in Bluetooth Physical/Radio Layer
Islam Galal
(islam.galal@bhit.bu.edu.eg)
Electrical Engineering Department
Benha Faculty of Engineering
Benha University
Prof. Dr. Abdelhalim Zekry
Dr. Mostafa E. A. Ibrahim
Dr. Hossam E. Ahmed

---
Outline
Outline
- Objectives
- Bluetooth Radio Specifications
- General Block Diagram of a Typical Bluetooth Physical Layer Transceiver.
- Utilized Modulation Techniques.
- Gaussian Frequency Shift Keying (GFSK).
- π/4 shifted Differential Quadrature Phase Shift Keying (π/4 - DQPSK).
- π/8 shifted Differential Eight Phase Shift Keying (π/8 – D8PSK).
- Frequency Hopping (FH).
- Transmitter Modulated Waveforms after Applying FH.
- BER Comparisons For All Simulated Systems.
- Conclusions.

---
Objectives
Objectives
- Provide a brief description of the Bluetooth standard including the Physical Layer.
- Achieve modulation with power efficient implementation , and Minimum Bit Error Rates.
- Give a high level view of the Radio Communication issues in various modulation schemes used by Bluetooth.
- Focus on developing MATLAB/SIMULINK models for the Different Bluetooth transceivers.

---
Bluetooth Radio Specifications
Bluetooth Physical Layer
Bluetooth Radio Specifications
Transmitter
  - Operates in the 2.4 GHz unlicensed ISM band.
  - 79 hop frequencies: f = 2402+k MHz, k= 0, 1, 2, ..., 78.
  - Nominal output power = 0 dBm (1 mW).
- Receiver
  - BER < 10-3 for GFSK:
    - –70dBm input power level.

---
General Block Diagram of a
General Block Diagram of a
Typical Bluetooth Physical Layer Transceiver

---
Utilized Modulation Techniques
Utilized Modulation Techniques
Gaussian Frequency Shift Keying (GFSK)
  - GFSK System Simulation Parameters.
  - Pulse shaping: Gaussian Pulse Shape Filter.
  - Impact of Gaussian Filter on Constellation Diagram, Time Domain Waveforms and Power Spectral Density (PSD).
  - GFSK BER Simulation Results

---
Utilized Modulation Techniques
Utilized Modulation Techniques
Continued…1
π/4 shifted Differential Quadrature Phase Shift Keying (π/4 - DQPSK)
  - π/4 - DQPSK System Simulation Parameters.
  - π/4 - DQPSK & π/8 – D8PSK Modulator/Demodulator.
  - Pulse shaping: Raised Cosine (RC) Filter.
  - Impact of RC Filter on Constellation Diagram, Time Domain Waveforms and Power Spectral Density.
  - π/4 - DQPSK BER Simulation Results

---
Utilized Modulation Techniques
Utilized Modulation Techniques
Continued…2
π/8 shifted Differential Eight Phase Shift Keying (π/4 – D8PSK)
  - π/8 – D8PSK System Simulation Parameters.
  - Impact of RC Filter on Constellation Diagram, Time Domain Waveforms and Power Spectral Density.
  - π/8 – D8PSK BER Simulation Results

---
GFSK System Simulation Parameters:
First: Gaussian Frequency Shift Keying (GFSK)
GFSK System Simulation Parameters:
Data Rate Rb	1Mbps
Modulation Index β	0.28 - 0:35
Frequency Deviation ∆F	140 - 175 KHz
Gaussian Filter With BT	0.5
Effective Signal Bandwidth 3dB	1MHZ
FHSS - AFH (79 frequencies)	2.402 + k MHz, k=0, …, 78 - 160 Khps - slot time = 6.25 uSec
Transmitting Bandwidth	2.400-2.4835 GHz
AWGN Channel
	Eb/No (e.g.)	5 dB
	Number of bits per symbol	1 bps
	Input signal power	2.5mW
	Symbol period	1uSec

---
Pulse Shaping: Gaussian Pulse Shape Filter
GFSK
Continued…1
Pulse Shaping: Gaussian Pulse Shape Filter
GFSK Modulator

---
Impact of Gaussian Filter on Constellation Diagram
GFSK
Continued…2
Impact of Gaussian Filter on Constellation Diagram

---
Impact of Gaussian Filter on Time Waveforms & PSD
GFSK
Continued…3
Impact of Gaussian Filter on Time Waveforms & PSD
Constant Envelope - Highly Power Efficient
Lower Adjacent Channel Emission

---
GFSK BER Simulation Results
GFSK
Continued…4
GFSK BER Simulation Results

---
π/4 - DQPSK System Simulation Parameters:
Second: π/4 shifted Differential Quadrature Phase Shift Keying
(π/4 - DQPSK)
π/4 - DQPSK System Simulation Parameters:
Data Rate Rb:	2Mbps
SRRC filter with Roll-off Factor α:	0.4
Effective Signal Bandwidth 3dB	1MHZ
FHSS - AFH (79 frequencies)	2.402 + k MHz, k=0, …, 78 - 160 Khps - slot time = 6.25 uSec
Transmitting Bandwidth	2.400-2.4835 GHz
AWGN Channel
	Eb/No (e.g.)	5 dB
	Number of bits per symbol	2 bps
	Input signal power	2.5mW
	Symbol period	1uSec

---
π/4 - DQPSK - π/8 – D8PSK Modulator / Demodulator
π/4 – DQPSK
Continued…1
π/4 - DQPSK - π/8 – D8PSK Modulator / Demodulator

---
Square Root Raised Cosine (SRRC) Filter
π/4 – DQPSK
Continued…2
Square Root Raised Cosine (SRRC) Filter
At alpha = 0 its Rect but duo to the divide by zero is not-permitted
Thus, in Matlab we devide by 0+1e-18

---
Impact of RC Filter on π/4 – DQPSK Constellation Diagram
π/4 – DQPSK
Continued…3
Impact of RC Filter on π/4 – DQPSK Constellation Diagram

---
Impact of RC Filter on Time Waveforms & PSD
π/4 – DQPSK
Continued…4
Impact of RC Filter on Time Waveforms & PSD
Lower Adjacent Channel Emission But Non-constant Envelope
Less Power Efficiency

---
RC π/4 - DQPSK BER Simulation Results
π/4 – DQPSK
Continued…5
RC π/4 - DQPSK BER Simulation Results

---
π/8 – D8PSK System Simulation Parameters:
Third: π/8 shifted Differential Eight Phase Shift Keying (π/8 – D8PSK)
π/8 – D8PSK System Simulation Parameters:
Data Rate Rb:	3Mbps
SRRC filter with Roll-off Factor α:	0.4
Effective Signal Bandwidth 3dB	1MHZ
FHSS - AFH (79 frequencies)	2.402 + k MHz, k=0, …, 78 - 160 Khps - slot time = 6.25 uSec
Transmitting Bandwidth	2.400-2.4835 GHz
AWGN Channel
	Eb/No (e.g.)	5 dB
	Number of bits per symbol	3 bps
	Input signal power	25mW
	Symbol period	1uSec

---
Impact of RC Filter on Time Waveforms & PSD
π/8 – D8PSK
Continued…1
Impact of RC Filter on Time Waveforms & PSD

---
Impact of RC Filter on π/8 – D8PSK Constellation Diagram
π/8 – D8PSK
Continued…2
Impact of RC Filter on π/8 – D8PSK Constellation Diagram

---
RC π/8 – D8PSK BER Simulation Results
π/8 – D8PSK
Continued…3
RC π/8 – D8PSK BER Simulation Results

---
Frequency Hopping (FH)
Frequency Hopping (FH)
FH occurs by jumping from one channel to another in pseudorandom sequence.
Resists interference and multipath effects.
Provides a form of multiple access among collocated devices in different piconets.
Total bandwidth divided into 1 MHz channels.

---
Transmitter Modulated Waveforms after Applying FH
Transmitter Modulated Waveforms after Applying FH

---
BER Comparisons For All Simulated Systems
BER Comparisons For All Simulated Systems

---
Conclusions
Conclusions
- In this work three different models for Bluetooth TX/RX with three different modulation schemes have been done.
- GFSK has the best power efficient transmission.
- Utilizing RC filter has better decay in side-loop suppressions than Gaussian filter.
- π/4 - DQPSK and π/8 - D8PSK modulation schemes have higher bandwidth efficiency compared to the GFSK.
- π/4 - DQPSK model achieves the best performance under AWGN channel
- This work is a first step towards a SDR-based implementation of the Bluetooth transceiver using USRP.

---
Thanks For Your Attention.
Thanks For Your Attention.
Questions??